BLU MAGIC MEMBRANE TANK            STEP BY STEP MAINTENANCE GUIDE

| Check the Pressure Settings. Turn-Off the electric supply of Water Pump. Close the Gate Valve coming from the source of water (supply going to the pump) Drain the Water inside the Blu Magic Tank, open the supply line until the Pressure Gauge turns to Zero (0) PSI Check the Pre-Charge Air of Blu Magic Tank using the Tire Gauge. Insert it to the Pin hole (upper side of the Blu Magic Tank). Pre-Charge Air must be 2 PSI lower than the Cut-in of Pressure Settings. For Example, Pressure Settings Pre-Charge Air Pressure Cut-In Cut-Off 20 40 18 PSI 30 50 28 PSI 40 60 38 PSI If the Pre-Charge Air is over charged, it can be lessen by pressing the pin hole. To get the System in operation after charging the Air. Open the Gate Valve coming from the source of water afterwards the electric supply, automatically the Water Pump will start to run | WARRANTY Two Years limited warranty provided it is use under normal working conditions Customer Name Receipt / Date Model / Serial No. Lapsed of Warranty Pressure Setting Installed by & Date WARNING Ang maling pag-aadjust ng Pre-Charge Air sa loob ng Blu Magic Tank ayon sa Cut-in ng Pressure Switch ay makakasira at tuluyang mapupunit ang Rubber Butyl Diaphragm o Bladder sa loob ng tangke. Sa ganitong pagkakataon hindi na ito sakop ng garantiya Kinakailangan din ang pagkabit ng Pressure Relief Valve dahil ang hindi pagkabit nito ay maaring maging sanhi ng pagkasira ng tangke sa oras na mag-malfunction ang pressure switch Iwasan ipuwesto ang Blu Magic Tank sa lugar na binabaha at naaarawan, lagyan ng bubong o maliit na bahay para sa tanke. Siguraduhin nakapatay ang linya ng kuryente sa tuwing magkakabit o aayusin ang inyong Water Pump at Blu Magic Tank CALL SUPERTANK SERVICE DEPT. 359-6-359 or 414-6-441 or VISIT US @ http://SUPERTANK.ph.tc |
| --- | --- |

# Text boxes

TIRE GAUGE

FOOT PUMP

BMI-6V to BMI-80V

AIR COMPRESSOR

BMI-120V to BMI-800V